Article 5.                Development Procedures

5.01	Purpose							                     Page 5-5

5.03	General Requirements                          				         Page 5-5

A. Requirements Applied Generally Throughout Article 5                         Page 5-5

B. Expiration of Approvals                                                                          Page 5-5

5.05	Consolidated Approvals                                       			         Page 5-5

5.07	UDO Text and Official Zoning Map Amendments			         Page 5-6

A. Definition                                                                                                Page 5-6

B. Amendment Process                                                                                Page 5-6

C. Standards for Approval                                                                           Page 5-6

D. Amendment Process Steps                                                                      Page 5-6

E. Submittal Requirements                                                                          Page 5-8

5.09	Development Approvals:  Categories and Criteria                   	         Page 5-8

A. General Requirements                                                                             Page 5-8

B. Accessory Use and Buildings – Major                                                    Page 5-8

C. Accessory Use and Buildings – Minor                                                    Page 5-9

D. Certificates of Zoning Compliance (CZC)                                             Page 5-9

E. Changes in Use                                                                                      Page 5-11

F. Conditional Use                                                                                     Page 5-11

G. Development Plan                                                                                 Page 5-12

H. Minor Modifications                                                                             Page 5-13

I. Final Plat                                                                                                 Page 5-13

J. Floodplain Permit                                                                                   Page 5-13

K. Landscape Plan                                                                                     Page 5-14

L. Lighting Plan                                                                                         Page 5-14

M. Sign Permit                                                                                           Page 5-14

N. Site Plan – Major                                                                                  Page 5-15

O. Site Plan – Minor                                                                                  Page 5-16

P. Subdivision – Major                                                                              Page 5-16

Q. Subdivision – Minor                                                                             Page 5-16

R. Temporary Use                                                                                     Page 5-17

S. Preliminary Plat                                                                                    Page 5-17

T. Variance                                                                                                Page 5-17

5.11	Development Approvals:  Procedure                                          	       Page 5-17

A. General Requirements                                                                           Page 5-17

B. Approvals by PEDD                                                                              Page 5-18

C. Approvals by Planning Commission                                                     Page 5-18

D. Floodplain Permit Procedure                                                                Page 5-20

E. Subdivision – Major                                                                              Page 5-21

F. Final Plat Amendment                                                                           Page 5-23

G. Vacation of Streets, Alleys, Easements                                                Page 5-24

5.13	Development Approvals:  Submittal Requirements                  	       Page 5-24

A. General                                                                                                  Page 5-24

B. Accessory Use – Major                                                                         Page 5-25

C. Accessory Use – Minor                                                                         Page 5-25

D. Certificate of Zoning Compliance                                                        Page 5-25

E. Change in Use                                                                                       Page 5-26

F. Conditional Use                                                                                     Page 5-26

G. Development Plan                                                                                 Page 5-26

H. Final Plat                                                                                               Page 5-29

I. Floodplain Permit                                                                                   Page 5-30

J. Landscape Plan – Major                                                                         Page 5-31

K. Landscape Plan – Minor                                                                       Page 5-32

L. Landscape Plan – Alternative                                                                Page 5-33

M. Lighting Plan                                                                                        Page 5-34

N. Sign Plan                                                                                               Page 5-34

O. Site Plan – Major                                                                                  Page 5-34

P. Site Plan – Minor                                                                                   Page 5-35

Q. Subdivision – Major                                                                              Page 5-36

R. Subdivision – Minor                                                                              Page 5-41

S. Temporary Use                                                                                      Page 5-42

5.15	Related Approvals:  Building and Occupancy Permits		       Page 5-42

A. Building Permit                                                                                     Page 5-42

B. Certificate of Occupancy Permit                                                           Page 5-43

5.17	Variance Procedure     						       Page 5-43

A. Definition                                                                                              Page 5-43

B. Variance Process                                                                                   Page 5-43

C. Expiration of the Variance                                                                    Page 5-44

D. Standards for Approval                                                                         Page 5-44

E. Submittal Requirements                                                                        Page 5-45

5.19	Appeal Procedure							       Page 5-45

A. Responsibility                                                                                       Page 5-45

B. Appeals to BZA                                                                                     Page 5-46

5.01 	Purpose

This Article outlines the procedures and information necessary to obtain development approvals.  It also establishes procedures for the appeal and review of determinations and decisions of the Planning Commission, Board of Zoning Appeals (BZA) and Planning and Economic Development Department (PEDD).

  - General Requirements

- The following requirements apply generally throughout this article:

      - All applications for Planning Commission or BZA approval will first be reviewed by the PEDD and may be reviewed by the Technical Review Committee (TRC), at the PEDD’s discretion.  The PEDD will prepare a report with recommendations and will make a presentation at the Planning Commission, or BZA meetings as appropriate;

      - Applications may be reviewed by Planning Commission in a regularly scheduled work session prior to the Commission’s regularly scheduled formal meeting as appropriate; and

      - Unless otherwise indicated within this UDO, all applications for permits or other approvals shall be made to the PEDD or PEDD’s designee.

- Expiration of Approvals

      - Approvals granted by the City shall expire if the work has not begun within one year from the date of approval.

      - If the work described in any Zoning Certificate has not been substantially completed within one year of the date of issuance thereof, said certificate shall expire and be cancelled by the PEDD and written notice shall be given to the owner and contractor.  Additional work shall not occur until a new Zoning Certificate is issued.

5.05	Consolidated Approvals

Where possible, this Section intends to accommodate the simultaneous processing of applications of different permits and approvals which may be required for the same development project in order to make the review process as short as possible.  Such possibilities for concurrent filing and processing of applications include, but are not limited to, the following:

- A conditional use along with a Development Plan or Major Site Plan;

- A rezoning along with a petition for annexation; and,

- Preliminary Plat along with a Final Plat per Section 5.09.

  - UDO Text and Official Zoning Map Amendments

- Definition:  Zoning amendments include amendments to the Official Zoning Map and/or to the UDO text.  A person, corporation, Planning Commission, or City Council may initiate amendments.  The PEDD, Planning Commission and City Council shall review amendments.

- Amendment Process:  Amendments may be initiated in one of the following ways:

- By the filing of an application to Planning Commission by the owners or agent of the owner of the property within the area proposed to be affected or changed by said amendment;

- By the adoption of a motion by the Planning Commission; or

- By the adoption of a motion by City Council and referral to the Planning Commission.

All text and map amendments shall follow the same procedure.  City Council initiated text or map amendments shall be referred to Planning Commission for recommendation prior to Council consideration.

- Standards for Approval:  The following criteria shall be followed in approving zoning map amendments to the UDO:

- That the zoning district classification and use of the land will not materially endanger the public health or safety;

- That the proposed zoning district classification and use of the land is reasonably necessary for the public health or general welfare, such as by enhancing the successful operation of the surrounding area in its basic community function or by providing an essential service to the community or region;

- That the proposed zoning district classification and use of the land will not substantially injure the value of the abutting property;

- That the proposed zoning district classification and use of the land will be in harmony with the scale, bulk, coverage, density, and character of the area of the neighborhood in which it is located;

- That the proposed zoning district classification and use of the land are appropriately located with respect to transportation facilities, utilities, fire and police protection, waste disposal, and similar characteristics; and

- That the proposed zoning district classification and use of the land will not cause undue traffic congestion or create a traffic hazard.

- Amendment Process Steps:  Amendments to the UDO text or map shall be submitted according to the following steps:

- Pre-application Meeting:  The applicant shall meet with the PEDD prior to submitting an application for an amendment.  The purpose of the meeting is to discuss the proposal and to provide feedback regarding applicable standards and requirements;

- Preliminary Review by the PEDD:  Upon receipt of an application, the PEDD shall, within 10 business days, review the application and determine whether it provides all necessary and required information.  If it is incomplete, the PEDD shall advise the applicant of the deficiencies and inform the applicant that no further action will be taken on the application until all necessary and required information has been provided.  If it is complete, the PEDD shall forward the application to the members of the TRC, if applicable.  A complete application package shall be forwarded to Planning Commission;

- Review by the TRC:  The members of the TRC shall review the application and forward comments within five (5) business days to the PEDD, who shall then forward the comments of the TRC to the Planning Commission;

- Public Hearing and Notice:  Within 10 business days of determining that an application contains all the necessary and required information, the City Clerk of Council shall place the application on a Planning Commission agenda and schedule a public hearing on the proposed amendment.  Notice of the hearing shall be provided at least once in one or more newspapers of general circulation in the City.  The notice shall be published at least seven business days before the date of the hearing.  The notice shall state the time and place of the hearing and a summary of the proposed amendment.  The Text of the proposed amendment, maps, and plans (if applicable) shall be on file for public examination in the office of the Clerk of Council;

- Notice to Property Owners:  If the proposed amendment intends to rezone a parcel or parcels, a written notice of the public hearing shall be provided to all property owners of property within 300 feet of the area proposed to be rezoned.  The applicant shall provide to the PEDD a list, based upon the County Auditor’s current tax lists, of all property owners within 300 feet of the area proposed to be rezoned.  The PEDD shall send such notice, by first class mail, at least 20 days before the date of the hearing addressed to the owners appearing on the County Auditor’s current tax list and to such other list verified by staff;

- Planning Commission Public Hearing:  The Planning Commission shall review the application at a public hearing and recommend action to the City Council;

- Planning Commission Recommendation:  The Planning Commission may recommend that the amendment be approved as requested, approved with modifications by the Planning Commission; or be denied.  Planning Commission shall indicate the specific reason(s) for its recommendation.  A recommendation for approval or approval with modifications shall be forwarded to the City Council in ordinance form;

- Notice by City Council and Public Hearing:  Following receipt of the recommendation from Planning Commission, the City Council shall introduce the proposed ordinance at a regular or special meeting in accordance with the provisions of the City Charter.  The City Clerk shall schedule a public hearing on the proposed amendment;

- Notice to Property Owners by City Council:  Notice of the public hearing shall be published at least once in one or more newspapers of general circulation in the City at least 30 days before the public hearing date;

- Action by City Council:  After the public hearing, the City Council shall, in ordinance form, adopt by a majority vote of the full membership of City Council the Planning Commission’s recommendation; deny the recommendation; or adopt some modification thereof; and

- Effective date:  The amendment shall be effective 30 days following approval by the City Council unless otherwise indicated by emergency legislation.

- Submittal Requirements:  The following information shall be submitted:

- The name(s), parcel address(s), mailing address(s), e-mail address(s) and telephone numbers of the applicant(s), and the property owner(s) or designated agent if other than the applicant(s);

- Legal documentation of the parcel(s) to be rezoned, drawn by a survey or registered in the State of Ohio;

- A statement of the reason(s) for the proposed amendment;

- Present use and zoning district;

- Proposed use and zoning district of the subject site plus all parcels within 500 feet;

- A vicinity map at a scale determined by the PEDD showing property lines, existing and proposed zoning, thoroughfares, and such other items as the PEDD may require;

- A list of the names and mailing addresses of all property owners of within 300 feet of the subject parcel(s) including any properties located in adjoining communities;

- The payment of the application fee as established by City Council; and

- Electronic files of all developments, plans, subdivisions and other required information in a format defined by the PEDD.

5.09	Development Approvals:  Categories and Criteria

- General Requirements:  The following table summarizes the development approvals permitted under the UDO.  The subsequent sections of the UDO define the applicable approval processes and submittal requirements.

- Accessory Use and Buildings – Major:  A Major Accessory Use is an accessory use that, because of its size, location, or intensity of activity, may have impact on adjacent property.  Accessory uses and buildings may be erected upon a lot on which a principal structure already exists.  The use of the accessory buildings must be secondary and incidental to the principal use. The BZA considers major accessory uses for approval.  See Section 9.39 for standards.

- Accessory Use and Buildings – Minor:  A Minor Accessory Use is an accessory use that will not have a significant impact on adjacent property.  Accessory uses and buildings may be erected upon a lot on which a principal structure already exists.  The use of the accessory building must be secondary and incidental to the principal use.  The PEDD considers minor accessory uses and buildings for approval.  See Section 9.39 for standards.

- Certificates of Zoning Compliance (CZC):  The Certificate of Zoning Compliance shall demonstrate that an approved development complies with the requirements of the UDO.  The CZC must be issued prior to allowing a building occupancy permit to be issued.  No building or other structure shall be erected, constructed, re-constructed, enlarged, moved or structurally altered, nor shall any excavation or site improvements be commenced, until the following has occurred:

  - The owner of the property involved or a person having an interest in such property and acting under written authority of the owner has applied for a CZC;

  - The application for a CZC shall include the submittal of a site plan as defined herein;

  - The PEDD or Planning Commission shall review and approve a CZC depending upon whether a major or a minor site plan is required; and

  - The PEDD has issued the CZC following approval of the site plan.

A CZC shall become void at the expiration of one year after the date of issuance unless a building permit has been issued and construction has begun.  If no construction has begun or the use has changed within one year of the date of the certificate, a new application and certificate shall be required.  Construction is deemed to begin when all necessary excavation and piers or footings of at least one principal building included in the plan have been completed.

Table 5.1:  Development Approvals

| Request | UDO Application | UDO Permit(s) Required Before Construction | Approval Authority | Initial Appeal | Second Appeal |
| --- | --- | --- | --- | --- | --- |
| Accessory Use, Major | Zoning Certificate Application | Certificate of Zoning Compliance (CZC) | BZA | Court of Common Pleas |  |
| Accessory Use, Minor | Zoning Certificate Application | CZC | PEDD | BZA | Court of Common Pleas |
| Certificate for Nonconformance | Certificate for Nonconformance | CZC | PEDD | BZA | Court of Common Pleas |
| Certificate of Zoning Compliance (CZC) | Certificate of Zoning Compliance (CZC) | CZC | PEDD | BZA | Court of Common Pleas |
| Change in Use | Change in Use | CZC | PEDD | BZA | Court of Common Pleas |
| Change in Nonconformity | Change in Use | CZC | Planning Commission | BZA | Court of Common Pleas |
| Conditional Use | Conditional Use | Conditional Use Certificate | BZA | Court of Common Pleas |  |
| Developmental Plan | Zoning Certificate Application | CZC | City Council | Court of Common Pleas |  |
| Floodplain Permit | Floodplain Permit | Floodplain Permit | PEDD and TRC | BZA | Court of Common Pleas |
| Landscape Plan, Major | Zoning Certificate Application | CZC | PEDD | BZA | Court of Common Pleas |
| Landscape Plan, Minor | Zoning Certificate Application | CZC | PEDD | BZA | Court of Common Pleas |
| Rezoning | Zoning Certificate Application | CZC | City Council | Court of Common Pleas |  |
| Sign | Zoning Certificate Application | CZC | PEDD | BZA | Court of Common Pleas |
| Site Plan, Major | Site Plan, Major | CZC | Planning Commission | BZA | Court of Common Pleas |
| Site Plan, Minor | Site Plan, Minor | CZC | PEDD | BZA | Court of Common Pleas |
| Subdivision, Major Preliminary Plat | Subdivision Application | Letter of Approval | Planning Commission | BZA | Court of Common Pleas |
| Subdivision, Major Final Plat | Subdivision Application | Mayor and Planning Commission Chair Signature on Record Plat | Planning Commission | BZA | Court of Common Pleas |
| Subdivision, Minor Lot Split | Subdivision Application | Signature of Planning and Zoning Administrator on Legal Description | PEDD | BZA | Court of Common Pleas |
| Temporary Use | Zoning Certificate Application | CZC | PEDD | BZA | Court of Common Pleas |
| Use Interpretation | Zoning Certificate Application | CZC | PEDD | BZA | Court of Common Pleas |
| UDO Interpretation | Zoning Certificate Application | CZC | PEDD | BZA | Court of Common Pleas |
| Variance | Variance Application | CZC | BZA | Court of Common Pleas |  |

- Changes in Use:  A change in the use of a building or structure may be approved by the PEDD if the use is substantially similar to the existing use or another permitted use under the existing zoning district classification as indicated on the Official Zoning Map.  A change in use may or may not involve interior or exterior building alterations.  An application must be filed.

- Conditional Use:  Conditional Uses are those uses that, because of special requirements or characteristics, may be allowed in a particular zoning district only after review by the BZA and the granting of Conditional Use approval imposing such conditions as necessary to make the use compatible with other uses permitted in the same district zone or vicinity.  A Conditional Use as listed in a particular zoning district shall be allowed in that zoning district after permission is granted by the BZA in accordance with the provisions of the UDO.

- Standards for Approval:  The following standards shall be considered in the review of Conditional Use Applications:

  - The Conditional Use is a use that may be permitted with conditions, in the District for which it is proposed;

  - The Conditional Use will be in accordance with the general objectives, or with any specific objective, of this UDO;

  - The Conditional Use will be designed, constructed, operated, and maintained so as to be harmonious and appropriate in appearance with the existing or intended character of the general vicinity and that such use will not change the essential character of the same area;

  - The Conditional Use will not be hazardous to or unreasonably disturbing to existing or future neighboring uses;

  - The Conditional Use will be served adequately by essential public facilities and services such as highways, streets, police and fire protection, drainage structures, refuse disposal, water and sewer, and schools; or that the persons or agencies responsible for the establishment of the proposed use shall be able to adequately provide any such services;

  - The Conditional Use will not create excessive additional requirements, at public cost, for public facilities and services and will not be detrimental to the economic welfare of the community;

  - The Conditional Use will not involve uses, activities, processes, materials, equipment and conditions or operations that will be detrimental to any persons, property, or the general welfare by reason of excessive production of traffic, noise, smoke, fumes, glare, negative appearance, or odors;

  - The Conditional Use will have vehicular approaches to the property, which shall be designed so as not to interfere with traffic on surrounding public thoroughfares; and

  - The Conditional Use will not result in the destruction, loss or damage of a natural, scenic, or historic feature of major importance.

- The BZA shall hold a public hearing on a Conditional Use in accordance with Section 5.07 D(1) – 5.07 D(5) of this UDO as it relates to the timelines, means, and methods of the Conditional Use Application being reviewed by City Staff, submitted for consideration by the BZA, and the necessary timelines, means, and methods in providing the general public notice of said public hearing.

- Action by the BZA:  After the public hearing, the BZA shall, by a majority vote of the full membership, approve; approve with conditions, or deny the requested Conditional Use application.

- In the event the BZA approves, or approves with conditions, a Conditional Use application, a Conditional Use Certificate, as issued by PEDD, shall authorize the conditional use on the specific parcel(s) for which it was approved.  The Conditional Use Certificate is non-assignable and shall expire one year from the date of enactment, unless prior to that date the applicant commences actual construction or business.  There shall be no modification of a Conditional Use Certificate except by the BZA.

- Development Plan:  Approval of a Development Plan is required within the Residential Planned Development (R-PD), Office Planned Development (O-PD), Business Planned Development (B-PD), Industrial Planned Development (I-PD) and the Mixed Use Overlay Districts including the Neighborhood Center (NC), Community Center (CC), and the Corporate Business (CB) Districts.

The two-step Development Plan review and approval process includes submission of a Preliminary Development Plan and a Final Development Plan.  The TRC and the Planning Commission review both plans.  Depending on the scope and complexity of the project proposed, the Planning Commission may permit the Preliminary Development Plan and the Final Development Plan to be combined as one submission.  That request should be made to and approved by the Planning Commission.

- Standards for Approval. The following standards shall be considered in the review of Development Plan applications:

  - It fully complies with the applicable requirements of the UDO;

  - It adequately protects other property or other uses located on the same property;

  - It is consistent with other development on nearby property;

  - It provides safe conditions for pedestrians or motorists and prevents a dangerous arrangement of pedestrian and vehicular ways; and

  - It provides safe ingress and egress to emergency vehicles on the site.

- The Planning Commission and City Council shall hold a public hearing on a Development Plan in accordance with Section 5.07 D of this UDO.

- Minor Modifications:  After the Final Development Plan has been approved by Planning Commission and prior to issuing a Certificate of Occupancy, adjustments or rearrangements of buildings, drives, parking areas, recreation areas, entrances, heights, yards, changes to the exterior façade, or similar modifications, may be requested by the applicant.  The PEDD shall review such amendments to a major site plan if the change involves 25 percent or less of the original gross floor area or lineal dimension, or 1,000 square feet whichever is less.  Amendments to a major site plan greater than this requirement shall be reviewed by the Planning Commission.

- Final Plat:  A final plat must be accepted by Planning Commission and recorded by the Montgomery County Recorder’s Office before lots may be transferred.

  - Standards for Approval:  The following standards shall be considered in the review of the Final Plat applications:

        - The Final Plat is in accordance with the Preliminary Plat and covenants are acceptable;

        - That the Final Plat is consistent with the approved Preliminary Plat;

        - That the Final Plat is consistent with the approved Development Plan;

        - The Director of Public Services and/or City Engineer has approved all construction;

        - The homeowners association and other agreements have been approved by the City Attorney’s Office;

        - The maintenance bonding requirements have been met; and

        - All fees have been paid.

- Floodplain Permit:  A Floodplain Permit shall be obtained before construction begins within any area of special flood hazard as defined in Section 9.37.D, Basis for Establishing the Areas of Special Flood Hazard.  Application for a Floodplain Permit shall be made on forms furnished and approved by the PEDD.

  - Standards for Approval:  The following  standards shall be considered in the review of Floodplain Permit applications:

        - The flood plain application does not include uses that are dangerous to health, safety and property;

        - The application includes uses that are protected against flood damage at the time of construction;

        - The alteration of stream channels, natural floodplains and protective barriers are controlled;

        - The filling, grading, dredging, and other development are sufficiently controlled; and

        - The proposed construction in floodplain does not cause additional flooding of adjacent property.

- Landscape Plan:  A Landscape Plan shall be submitted as part of the site plan review process.  Such plans shall be reviewed and approved by the PEDD.

  - Standards for Approval:  The following standards shall be considered in the review of Landscape Plan applications:

        - The Landscape Plan meets all the requirements and fulfills the purposes and intent of the UDO;

        - The Landscape Plan is in concurrence with relevant City plans and policies;

        - The public’s health, safety and welfare will not be adversely impacted by the proposal; and

        - The plant materials are approved by the City, including sufficiency.

- Lighting Plan:  Prior to the approval of a Building Permit, Occupancy Permit, or Certificate of Zoning Compliance, a plan demonstrating compliance with the exterior lighting standards of Section 9.27 will be submitted and approved by the PEDD.

  - Standards for Approval:  The following standards shall be considered in review of Lighting Plan applications:

        - The Lighting Plan meets all the requirements and fulfills the purpose and intent of the UDO;

        - The Lighting Plan is in concurrence with relevant City plans and policies;

        - The public’s health, safety and welfare will not be adversely impacted by the proposal; and

        - The exterior lighting meets illumination standards.

- Sign Permit:  No sign, whether permanent or temporary, shall hereafter be erected, constructed or maintained until the PEDD has issued a sign permit.  This provision shall not apply to signs described in Section 9.51.C.  The application for a sign permit shall be a Certificate of Zoning Compliance as defined in Article 11.

  - Standards for Approval:  The following standards shall be considered in the review of Sign Permit applications:

        - The Sign Permit application meets all the requirements and fulfills the purposes and intent of the UDO;

        - The Sign Permit application is in concurrence with relevant City plans and policies; and

        - The public’s health, safety and welfare will not be adversely impacted by the proposal.

- Site Plan – Major:  Approval of a Site Plan is required for zoning approval prior to construction.  Planning Commission shall review all applications that do not meet the definition of a Minor Site Plan as provided for in Section 5.09.O.

  - Uses Requiring Major Site Plan Review:  The following uses and additions to uses require major site plan review:

        - Multi-family buildings four units and above;

        - Commercial, office, industrial and all other non-residential buildings and structures, including principal and accessory structures;

        - Additions greater than 25 percent or 1,000 square feet of the original floor area, whichever is less;

        - Parking structures and facilities and parking lots;

        - Public buildings and structures (including parks) but to exclude any such facilities as owned and/or operated by the City of Riverside;

        - Institutional uses.

  - Standards for Approval:  The following standards shall be considered in the review of Major Site Plan applications:

        - That it fully complies with all applicable requirements of the UDO;

        - That it adequately protects other property  or residential uses located on the same property from the potential adverse effects of a non-residential use;

        - That it is consistent with the use and character of surrounding properties;

        - That it provides safe conditions for pedestrians or motorists and prevents the dangerous arrangement of pedestrian and vehicular ways; and

        - That it provides safe ingress and egress for emergency services.

  - Following approval of a Major Site Plan by the Planning Commission, the PEDD shall issue a CZC based on the plans approved, as amended, by the Planning Commission.  The PEDD shall approve amendments to Major Site Plans if the change involves 25 percent or less of the original floor area, not to exceed 5,000 square feet.

- Site Plan – Minor:  Approval of a Site Plan is required for zoning approval prior to construction.  The PEDD shall review any application for a Minor Site Plan in accordance with the Standards for Approval contained in Section 5.09 N. Site Plan – Major of this UDO.

- Subdivision – Major:  A Major Subdivision is a platting of land for the purposes of development and transfer of ownership.  It requires approval of a Preliminary Plat and Final Plat by the Planning Commission and recording of the final plat prior to the transfer of land.

  - Standards for Approval:  The following standards shall be considered in the review of Major Subdivision applications:

        - The proposed subdivision meets all applicable standards of the UDO;

        - The proposed lots in the subdivision shall have adequate space to accommodate the building area and other site requirements;

        - The property has been surveyed and a record plat prepared including original plat mylars and other information relating to the property has been submitted with the application including electronic copies;

        - The proposed lots have been approved for access management, utility management and storm-water management; and

        - The proposed lots have been approved relative to emergency access.

- Subdivision – Minor:  A Minor Subdivision or lot split is a division of a single parcel of land or lot with no public improvements that is approved by the PEDD and does not require a plat to be approved by Planning Commission.

  - Standards for Approval:  The following standards shall be considered in the review of Minor Subdivision applications:

        - The proposed subdivision meets all applicable standards of the UDO;

        - The proposed subdivision shall have adequate area to accommodate the building area and other site requirements;

        - The property has been surveyed and an acceptable drawing, legal description and other information relating to the property has been submitted with the application;

        - The proposed lot has been approved for access management and storm-water management; and

        - The proposed lot has been approved relative to emergency access.

- Temporary Use:  The PEDD may approve a temporary use.

  - Standards for Approval:  The following standards shall be considered in the review of Temporary Use applications:

        - The proposed Temporary Use meets all requirements of the UDO;

        - The site, if undeveloped, contains sufficient open space to support the Temporary Use;

        - The location of the Temporary Use on a site, if developed, shall be placed in a manner that does not interfere with the function of the permanent use;

        - The Temporary Use has sufficient off-street parking in a manner outlined in the UDO; and

        - The public’s health, safety and welfare on and around the Temporary Use are assured.

- Preliminary Plat:  A preliminary plat shall be approved by the Planning Commission prior to submitting a Final Plat.  A Preliminary Plat is a map of a subdivision of land that is submitted to the Planning Commission for purposes of preliminary consideration and approval.

  - Standards for Approval:  The following standards shall be considered in the review of a Preliminary Plat application:

        - The proposed Preliminary Plat meets all applicable standards of the UDO;

        - The proposed lots shall have adequate space to accommodate the building area and other site requirements;

        - The property has been surveyed to provide boundary, topographic, utility and other information relating to the property; which shall be submitted with the application;

        - The proposed lots have been approved for access management, utility management and storm-water management; and

        - The proposed lots have been approved relative to emergency access.

- Variance:  A Variance involves permission to depart from the literal requirements of the UDO.  The BZA shall consider and decide on any Non-Use Variance of this UDO.  The procedures for considering a Variance are included in Section 5.17.

  - Development Approvals:  Procedure

- General Requirements:  This Section of the UDO outlines a series of actions that are required for specific development approvals.  These actions are:

  - Approvals by the PEDD;

  - Approvals by Planning Commission;

  - Floodplain permit process;

  - Major subdivision process; and

  - Minor subdivision process.

- Approvals by PEDD:  The following outlines the procedure under which the PEDD decides development approvals:

- Pre-application Meeting:  The applicant shall meet with the PEDD prior to submitting an application for plan approval.  The purpose of the meeting is to discuss the proposal and to provide feedback regarding applicable standards and requirements.

- Formal Application Submittal:  The applicant shall submit an application that meets all of the applicable requirements of the UDO.  This shall occur consistent with the submittal schedule indicating application submittal and meeting dates established by the PEDD.

- Application Certification by PEDD:  Upon receipt of an application, the PEDD shall, within five days, review the application as to completeness.  If it is incomplete, the PEDD shall advise the applicant of the deficiencies and shall not process the application until the deficiency is corrected.  If it is complete and appropriate in the PEDD’s professional judgment, the application shall be forwarded to the TRC, if applicable.

- Review by the TRC:  Members of the TRC may review the application and provide comments within five days to the PEDD.

- Action by the PEDD:  Within 15 days of a complete application’s acceptance, the PEDD shall render a decision to approve, approve with conditions, or deny an application.  The decision shall be communicated by permit, Certificate of Zoning Compliance or letter to the applicant citing the reasons for the decision.

- Appeal:  The decision by the PEDD can be appealed to the Planning Commission per Section 5.19.

- Approvals by Planning Commission:  The following outlines the procedure under which Planning Commission decides development approvals:

- Pre-application Meeting:  The applicant shall meet with the PEDD prior to submitting an application.  The purpose of the meeting is to discuss the proposal and to provide feedback regarding applicable standards and requirements.

- Formal Application Submittal:  The applicant shall submit an application meeting all of the applicable requirements of the UDO.  This submittal shall occur consistent with the meeting dates and submittal schedule established by the Planning Commission.

- Application Certification by PEDD:  Upon receipt of an application, the PEDD shall, within five days, review the application as to completeness.  If it is incomplete, the PEDD shall advise the applicant of the deficiencies and shall not process the application until the deficiency is corrected.  If it is complete, the PEDD shall forward the application to the TRC, if applicable.

- Preparation of Agenda and Public Notice:  Following certification that an application is complete, the PEDD shall place the application on the agenda of Planning Commission’s formal meeting.  Major Site Plan applications requiring Planning Commission approval are not subject to notification procedures.

  - Notice of the hearing shall be given at least once in one or more newspapers of general circulation in the City.  Notice shall be at least 10 days before the date of the hearing.  The notice shall state the time and place of the hearing and a summary of the proposed amendment;

  - The applicant shall provide a list (available from the County Auditor’s current tax list) of the owners within 300 feet of the subject area proposed to be rezoned to the PEDD.  Such notice shall be sent, by the applicant by first class mail, at least 10 days before the date of the hearing addressed to the owners appearing on the County Auditor’s current tax list and to such other list or lists as verified by staff.  The notice shall contain the same information as required of notices published in newspapers as specified; and

  - The application, staff recommendation and associated material shall be on file for public examination in the office of the PEDD.

- Review by TRC:  Members of the TRC may review the application at a meeting and provide comments within five days to the PEDD.

- Preparation of Staff Report:  The PEDD shall prepare a staff report providing an analysis of the proposal and a recommendation.  The PEDD shall consider comments from the TRC in formulating a recommendation.  The application and written report shall be forwarded to the Planning Commission prior to the meeting at which the Planning Commission will consider the application.

- Action by the Planning Commission:  The Planning Commission shall consider the application at its formal public meeting.  It shall hear a presentation by staff as appropriate, a presentation by the applicant, and comments by interested parties.  The Planning Commission shall consider this information and render a decision at the public meeting.  If necessary, it can table and continue hearing the application for no more than 60 days with the concurrence or the applicant, at which time it shall render a decision.  In rendering a decision, the Planning Commission shall consider the applicable decision criteria of this UDO.  The Planning Commission shall approve, approve with conditions or deny an application.  Its decision shall take effect immediately.

- Floodplain Permit Procedure: The PEDD is hereby appointed to administer and implement the UDO by granting or denying floodplain permit applications in accordance with its provisions.

- Procedure:  The PEDD shall:

  - Review all floodplain permits to determine that the permit requirements of the UDO have been satisfied;

  - Review all floodplain permits to assure that all necessary permits have been received from those Federal, State or Local governmental agencies from which prior approval is required.  The applicant shall be responsible for obtaining such permits, as required, including permits issued by the Department of the Army under Section 10 of the Rivers and Harbors Act and Section 404 of the Clean Water Act;

  - Review all floodplain permits to determine if the proposed development is located within a designated floodway.  Floodways are delineated on the Flood Insurance Rate Map (FIRM) as prepared and maintained by the Federal Emergency Management Agency (FEMA).  Floodways may also be delineated in other sources of flood information;

  - If the proposed development is located within a designated floodway, assure that the encroachment complies with the provisions of Section 9.37; and

  - If determined as appropriate, submit an application for a floodplain permit to the TRC for review prior to his or her approval.

- Use of other Base Flood Elevation and Floodway Data:  Areas of special flood hazard where base flood elevation data have not been provided by FEMA, in accordance with Section 9.37, Basis for Establishing the Areas of Special Flood Hazard, are designated as Zone A on the FIRM.  Within these areas, the PEDD shall obtain, review and reasonably utilize any base flood elevation and floodway data available from a Federal, State or other source.

- Information to be Obtained and Maintained:  Where base flood elevation data are utilized within areas of special flood hazard on the FIRM, regardless of the source of such data, the following provisions apply:

- Obtain and record the actual elevation (in relation to mean sea level) of the lowest floor, including basement, of all new or substantially improved structures, and whether or not such structures contain an enclosure below the lowest floor; and

- For all new or substantially improved flood proofed non-residential structures:  verify and record the actual elevation (in relation to mean sea level) to which the structure was flood proofed; maintain the flood proofing certifications required in Section 9.37; and maintain for public inspection all records pertaining to the provisions of the UDO.

- Alteration of Watercourse:  The PEDD shall also:

- Notify adjacent communities and the Ohio Department of Natural Resources, Division of Water, prior to any alteration or relocation of a watercourse and submit evidence of such notification to FEMA.  A watercourse is considered to be altered, if any change occurs within its banks;

- Maintain engineering documentation required in Section 9.37 that the flood carrying capacity of the altered or relocated portion of said watercourse will not be diminished;

- Require that necessary initial construction and maintenance will be provided for that altered or relocated portion of said watercourse so that it remains where planned and the flood carrying capacity will not be diminished; and

- Make interpretations, where needed, as to the exact location of the boundaries of the areas of special flood hazards (for example, where there appears to be a conflict between a mapped boundary and actual field conditions).  The person contesting the location of the boundary shall be given a reasonable opportunity to appeal the interpretation as provided in Section 5.19 of this UDO.

- Subdivision – Major:  Before any land is subdivided the owner of the property proposed to be subdivided, or his/her/its authorized agent, shall apply for and secure approval of the proposed subdivision in accordance with the following procedures, which include a Preliminary Plat and Final Plat.

- Preliminary Plat Pre-application Meeting:  The developer/ subdivider shall meet with the PEDD prior to submitting a Preliminary Plat for consideration by the Planning Commission.  Following the conclusion of the meeting, the PEDD shall forward to the developer/subdivider a written summary of the results of the pre-application meeting including recommendations and all attached comments.

- Preliminary Plat Review by PEDD:  Upon receipt of an application, the PEDD shall, within five days, review the application as to completeness.  If it is incomplete, the PEDD shall advise the applicant of the deficiencies and shall not process the application until all the necessary required information has been provided.  If the application is complete, the PEDD may submit the application to the TRC.

- Preliminary Plat Review by the TRC:  The TRC shall review the application after the PEDD determines that the application is complete and forward its comments within five days to the PEDD.  The PEDD shall forward copies of all documents filed with the PEDD to the Planning Commission along with any report or recommendation of the TRC.

- Planning Commission Approval:  The Planning Commission shall review the application and decide the Preliminary Plat be approved as requested; that the Preliminary Plat be approved as modified by the Planning Commission; or that the Preliminary Plat be denied.  The decision of the Planning Commission shall indicate the specific reason(s) upon which the recommendation is based.

- Plan Re-submittal:  The developer/ subdivider shall submit a reproducible original Preliminary Plat meeting the approval and conditions of the Planning Commission to the PEDD for approval and signature.  The Preliminary Plat shall meet the submittal requirements of Section 5.13(a).

- Expiration:  The approval of a Preliminary Plat by the Planning Commission shall be effective for a maximum period of 12 months and shall guarantee that the terms under which the approval was granted will not be affected by changes to the UDO.  If after this 12 month period, any phase(s) or portion(s) of the original approved Preliminary Plat has not received Final Plat approval, then no Final Plat approval will be given unless one six-month extension of the Preliminary Plat approval is requested in writing to and granted by the Planning Commission prior to the expiration date.  The Planning Commission may grant no more than one six-month extension.

- Construction Drawings:  Three sets and one digital copy of construction drawings for all improvements shall be provided to the Director of Public Services per the City Engineer’s requirements.

- Final Plat Pre-application Meeting:  The developer/ subdivider is encouraged to meet with the PEDD prior to submitting a Final Plat for consideration by the Planning Commission.  Following the conclusion of the meeting, the PEDD shall forward to the developer/ subdivider a written summary of the results of the pre-application meeting including recommendations and all attached comments.

- Final Plat Review by PEDD:  Upon receipt of an application, the PEDD or a designated representative shall, within five business days, review the application and determine whether it provides all necessary and required information.  If it is incomplete, the PEDD shall advise the applicant of the deficiencies and inform the applicant that no further action will be taken on the application until all necessary and required information has been submitted.

- Final Plat Review by TRC:  The TRC may review the application after the PEDD determines that the application is complete and forward its comments within five days to the PEDD.  The PEDD shall forward copies of all documents filed with the PEDD to the Planning Commission along with any report or recommendation of the TRC.

- Planning Commission Meeting and Approval:  The Planning Commission shall, within 30 days after the public meeting, approve the Final Plat as requested; that the Final Plat be approved as modified by the Planning Commission; or that the Final Plat be denied.  The decision of the Planning Commission shall indicate the specific reason(s) upon which their decision is based.

- Recording of Final Plat:  Once a Final Plat has been approved by Planning Commission, the developer/ subdivider shall make all modifications to the original mylars.  Once complete, the original mylars shall be forwarded to the PEDD for processing.  All Final Plats must be recorded within 12 months of the date of approval.  Final Plats may not be recorded until all required signatures of officials have been placed on the Final Plat.  If not recorded, all Final Plats shall officially expire after 12 months from the date of signature by the appropriate officials.  Once the Final Plat has been properly signed by the appropriate officials, the applicant can file the Final Plat with the Montgomery County Recorder, which shall process the Final Plat prior to its recording.  Once processed by the Map Office, the Final Plat will be forwarded to the County Recorder’s Office.  Once recorded, the original mylars of the Final Plat shall be filed with the City Engineer.

- Expedited Subdivision Procedure:  In cases where the proposed subdivision includes less than 10 lots and can be developed in one phase, the application does not warrant the full submittal procedure as determined by the PEDD.  If so determined, the applicant may combine the Final Development Plan, as outlined in Section 5.13.G and in the Final Plat procedures.  In doing so the same procedural steps will occur, however, a single set of documents for both the Development Plan and Final Plat will be submitted as directed by the PEDD.  The timeframe for review and approval of a Major Subdivision under this procedure shall be consistent with the general timeframe as provided in Section 5.11. E.

- Single Lot Major Subdivisions:  Major Subdivision plats that consist of one lot may be submitted to the City under this procedure.  The PEDD is hereby authorized to review and approve single lot Major Subdivisions.  The decision of the PEDD can be appealed to the Planning Commission.  The PEDD can submit the Preliminary Plat and Final Plat as a single set of documents to the TRC for review and approval.  The PEDD will identify the appropriate documents for submittal.  The timeframe for review and approval of a Major Subdivision under this procedure shall be consistent with the general timeframe as provided in Section 5.11.E.

- Final Plat Amendment:  Upon the application of an owner(s) of land described in a Final Plat, the Planning Commission may amend the Final Plat, in whole or in part, where unusual or exceptional factors or conditions require the amendment to avoid undue hardship.

- Plat Amendment Defined:  A plat amendment is the alteration of a Final Plat that changes any of the feature(s) required to be set forth in the plat by Section 5.11.E.(11).  The vacation or alteration of any street, road, highway, alley or easement by the City is not a plat amendment subject to the requirements of this section.

- Filing Requirements:  The applicant(s) shall file with the PEDD a Final Plat amendment which meets the requirements of this Section and other City ordinances as applicable, together with an application for approval thereof, an original mylar, and a fee for the review of said plat amendment.

- Procedure:  The procedure for a Final Plat amendment shall be as follows:

  - The applicant(s) shall file with the PEDD an application including required submittals, which sets forth the location and description of the proposed plat amendment and the reason(s) why the amendment of the plat is sought.  A copy of the application shall be filed along with the required sets of amended plat drawings proposed by the applicant(s); and

  - The City shall give 30 days notice of the proposed plat amendment application by publication in a newspaper of general circulation.  Such notices shall set forth the part or the plat to be amended and briefly describe the proposed amendment, the date(s) of the Planning Commission meeting hearing(s) on the application and the date(s) City Council will consider the application.  Notices for the Planning Commission and Council meetings shall be published separately for each meeting.

- Letter of Adequacy:  Within five days after the Final Plat amendment application has been filed with the PEDD, a copy thereof may be transmitted to the TRC, who will check said plat to determine adequacy with existing street, storm, sanitary, water and utility services.  If said final plat amendment does so conform, the TRC, within 10 days after said plat has been transmitted to him/her, will return said plat to the PEDD, together with a report verifying adequacy of the proposed amendment.  The PEDD shall thereupon transmit the report to the Planning Commission for its consideration.

- Planning Commission Review:  At the first meeting of the Planning Commission and after a copy of the Final Plat amendment application, together with the staff report and recommendation, has been received by the Planning Commission, it shall consider the Final Plat amendment and the Planning Commission shall take action regarding the plat amendment request.  If the final plat amendment is approved by Planning Commission, the applicant(s) shall follow all Final Plat filing requirements.  Inclusive of the approved amendment.

- Vacation of Streets, Alleys, Easements:  City Council may, by ordinance, vacate or alter any street, road, highway, alley or easement upon finding that there is good cause for such vacation or alteration.  Any such vacation or alteration shall first be reviewed by the PEDD, in order to make a recommendation to City Council.  Notice of the intention of Council to vacate or alter any street, road, highway, alley or easement shall be published in a newspaper of general circulation in the City for 45 days preceding such action unless all abutting landowners have filed written statements of consent to the proposed action with the City Clerk of Council, in which case no notice is required.  Any application to vacate or alter any street, road, highway, alley or easement shall be accompanied by a fee.

5.13	Development Approvals:  Submittal Requirements

- General:  The following general requirements shall apply:

  - Each development approval shall include an application provided by the PEDD with the submittal;

  - The City shall process only complete applications.  The PEDD shall make determination as to completeness;

  - The PEDD may request additional supporting information that in his/ her professional judgment is necessary to fully explain the applicant’s proposal.  The applicant shall supply the requested additional information; and

  - The full application fee shall be presented to the City with the application.

- Accessory Use – Major:  The submittal for approval of a Major Accessory Use shall include an application form for an Accessory Use – Major/Certificate of Zoning Compliance, a Major Site Plan, related materials, and fee.  The application shall include at a minimum:

- Name and mailing address of the current property owner or designated agent;

- Property address, parcel identification number and zoning classification of the subject property;

- Description of the existing and proposed use;

- Extent of any proposed interior building alterations that may be required as a result of the change in use; and

- A list of the surrounding uses and zoning classification(s).

- Accessory Use – Minor:  The submittal for approval of a Minor Accessory Use shall include an application form for an Accessory Use – Minor/Certificate of Zoning Compliance, a Minor Site Plan, related materials, and fee.  The application shall include at a minimum:

- Name and mailing address of the current property owner or designated agent;

- Property address, parcel identification number and zoning classification of the subject property;

- Description of the existing and proposed use;

- Extent of any proposed interior or exterior building alterations that may be required as a result of the change in use; and

- A list of the surrounding uses and zoning classification(s).

- Certificate of Zoning Compliance:  The submittal of a Certificate of Zoning Compliance shall include an application and the appropriate Site Plan (Major or Minor as applicable).  The application shall include at a minimum:

- Name and mailing address of the current property owner or designated agent;

- Name of applicant.  If the applicant is not the owner than written consent from the owner should be submitted;

- Address, parcel identification number, and zoning classification of the subject property;

- Description of the existing and proposed use;

- Extent of any proposed interior or exterior building alterations that may be required as a result of the change in use; and

- A list of the surrounding uses and zoning classification(s).

- Change in Use:  The submittal for approval of a Change in Use shall include an application form for a Change in Use with related materials and fee.  The application shall include at a minimum:

- Name and address of the current property owner or designated agent;

- Name of applicant.  If the applicant is not the owner than written consent from the owner should be submitted;

- Address, parcel identification number, and zoning classification of the subject property;

- Description of the existing and proposed use;

- Extent of any proposed interior or exterior building alterations that may be required as a result of the change in use; and

- A list of the surrounding uses and zoning classification(s).

- Conditional Use:  The submittal for approval of a Conditional Use shall include an application form for a Conditional Use with related materials and fee.  The application shall include at a minimum:

- Name and address of the current property owner or designated agent;

- Name of applicant.  If the applicant is not the owner then written consent from the owner should be submitted;

- Property address, parcel identification number, and zoning classification of the subject property;

- A site plan and other drawings to scale including a digital image of all plans, showing the existing and proposed use of the site, all pertinent natural and man-made features, and adjacent development character and buildings;

- A statement of need for the proposed use, its location and a report identifying the effects of the proposed use on the surrounding properties and the neighborhood; and

- A plan of how the potential negative effects of the proposed use will be mitigated including traffic, parking, noise, light intrusion, solid waste storage, odor, fumes and removal.

- Development Plan:  The following outlines the submittal requirements for Preliminary and Final Development Plan.  Relative to the approval process, each Preliminary and Final Development Plan must be approved through the same process.

- Preliminary Development Plan:  Application for a Preliminary Development Plan shall be provided at the time of submittal.  The Preliminary Development Plan shall be comprised of the following information:

  - A general supporting statement.  This is a narrative that explains what is being proposed and why.  The narrative shall explain the development proposal in context of existing structures on the property and adjoining properties and shall provide the approximate allocation of land use by acreage and type and shall provide an estimate of the population of the project at build-out;

  - An existing conditions plan at a scale determined by the PEDD indicating existing topography, property boundaries, trees, structures, pavements, utilities, and the location of existing directly adjacent properties and their structures;

  - Proposed site plan at a scale determined by the PEDD indicating pavement, structures, service areas, loading areas, parking circulation, trash dumpsters, setbacks, vegetation to remain, points of access, proposed grading required screens and buffers, and related site improvements.  This plan shall include the location of existing contiguous properties and their structures;

  - Conceptual architectural design and landscape planting;

  - Longitudinal and transverse cross-sections through the building at its tallest point.  These sections shall include contiguous property and their principal buildings to illustrate neighboring height relationships.  The scale of these sections shall be determined by the PEDD;

  - Engineering feasibility comments, report or study from a civil engineer for water, sanitary sewer and storm water utilities, traffic flow impacts; and

  - All plan documents should be accompanied by digital images in a format accepted by the PEDD.

- Final Development Plan:  Application for a Final Development Plan shall be provided at the time of submittal.  In addition to the Preliminary Development Plan requirements outlined in Section 5.13.G above, the Final Development Plan shall include the following:

- Boundaries of the tract and legal description;

- Locations of buildings, streets, drives and parking areas.  Locations and dimensions of right-of-ways, easements and all land to be dedicated to the City or reserved for specific uses;

- Proposed building floor plans at 1/8 inch equals one foot;

- Proposed building elevations at 1/8 inch equals one foot;

- Proposed exterior material schedule which identifies all exterior and site structure materials and color, including brick and stone;

- Illustration of general architectural concepts including perspective renderings and building/site cross-sections, which may be needed to explain concepts, if applicable or requested;

- Location of existing trees or tree cover that will remain.  Location of all individual trees on the site plan with diameters/calipers of six inches or greater;

- Location of public utility services, including storm drainage;

- Indicate whether streets and utilities are to be publicly or privately owned and maintained;

- The location and dimensions of right-of-ways, easements and all lands to be dedicated to the City or reserved for specific uses;

- Location of proposed construction limits and areas to remain undisturbed;

- Proposed landscape plan prepared by a registered engineer, architect, or landscape architect, as defined by Article 11 integrated with a grading plan, at a scale determined by the PEDD indicating existing trees to be saved, new plantings, and a schedule of plant material showing proposed sizes and quantities;

- Location, dimensions, (including height, square feet and language) and elevations of all signs;

- Exterior lighting plan and specifications including light color temperature, cut-off angle, distribution plan, intensity in foot-candle value within the light distribution area produced by the fixture(s) proposed, and the values of these foot-candle levels at all property lines;

- Longitudinal and transverse cross-sections through the building at its tallest point.  The sections shall include contiguous property and their principal buildings to illustrate neighboring height relationships.  The scale of these sections shall be determined by the PEDD;

- Grading plan including storm drainage plans drawn by a licensed civil engineer;

- Engineering plans for sanitary sewer, storm sewer and pavements by a licensed civil engineer;

- A plat of the proposed development area showing street right-of-way, subdivided and common land and easements in accordance with the requirements of the UDO which shall be in form for recording; and

- A text describing the character of the proposed development and includes standards that are supplemental to, and supportive of, the development standards contained within in the UDO.

- Effect of Approval:  Detailed Site Plan approval is assured based on good faith compliance with the approved Development Plan.  The approval shall be for a period of two years to allow for the submission of a Certificate of Zoning Compliance.  Unless the required Certificate of Zoning Compliance is properly submitted and approved within the two-year period, the approval shall be voided unless written request for time extension is submitted to and approved by the Planning Commission.  Such an extension shall not exceed six months.

- Final Plat:  An application form shall be completed by the developer/subdivider and submitted with the Final Plat.  The application form shall be provided by the PEDD.  The required fees shall be paid at the time of application submittal.  The following supplementary information shall be supplied in addition to these requirements:

- Boundary Lines:  All plat boundary lines with lengths of courses to hundredths of a foot and bearings to half minutes.  These boundaries shall be determined by an accurate survey in the field, which shall be balanced and closed with an error of closure of not to exceed one to ten thousand.

- Recorded Streets:  The exact location and the width along the property line of all existing recorded streets intersecting or paralleling the boundaries of the tract.

- Bearings:  True bearings and distances to nearest established street bounds, patent or other established survey lines, or other official monuments, which monuments shall be located or accurately described on the plat.  Any patent or other established survey or corporation lines shall be accurately monument-marked and located on the plat, and their names shall be lettered on them.

- Monuments:  The accurate location and material of all permanent reference monuments.

- Site Layout:  The exact layout including:

  - Streets and alley lines – their names, bearings, angles of intersection and widths (including widths along the line of any obliquely-intersecting street);

  - The chord length of all arcs – radii, points of curvature and tangent bearings;

  - All easements and right-of-ways, when provided for or owned by public services (with the limitation of the easement rights definitely stated on the plat); and

  - All lot lines with dimensions in feet and hundredths, and with bearings and angles to degrees, minutes and seconds if other than right angles to the street and alley lines.

- Lot Numbers:  Lots shall be numbered in numerical order.

- Property Offered for Dedication:  The accurate outline of all property which is offered for dedication for public use, and of all property that may be reserved by covenant in the deeds for the common use of the property owners in the subdivisions, with the purpose indicated thereon.  All lands dedicated to public use other than streets or roads shall be marked “Dedicated to the Public”.  Streets and roads not dedicated shall be marked “Private Street.”

- Setback Lines:  As shown on the preliminary plat.  Side and rear setbacks marked “for reference only” do not constitute a separate covenant.

- Name of Subdivision:  Name of subdivision and name or number of the largest subdivision or tract of which the tract now subdivided, forms a part and section number, if part of a larger subdivision.

- Adjoining Subdivision:  Names and locations of adjoining subdivisions and location and ownership of adjoining un-subdivided property.

- Names of Owners:  Names and addresses of the owner of record, the subdivider, and of the engineer or surveyor.

- All record plats shall include a north arrow, scale, date and title.

- Engineer’s Certificate:  A certificate by a registered professional engineer or surveyor to the effect that said plat was prepared by him, pursuant to an actual survey of the premises and that said plat is correct.

- Owner’s Certificate:  A certificate by the owner of the land to the effect that he has caused said land to be platted and that he dedicates to public use the streets, open space and other lands indicated on the plat as intended for public use.  The certificate shall be executed as a conveyance is executed.

- Bond, Letter of Credit or Certificate to Ensure Street Construction:  Security that is accepted by the City to ensure that street improvements will be satisfactorily completed.

- Floodplain Permit:  Application for a Floodplain Permit shall be made on forms, furnished by the PEDD and may include but not be limited to:  site specifics topographic plans drawn to scale showing the nature, location, dimensions and elevations of the area in question; and existing or proposed structures, fill, storage of materials, drainage facilities and the location of the foregoing.  A Floodplain Permit shall be provided at the time of submittal.  The following information is required:

- Elevation in relation to mean sea level of the lowest floor, including basement, of all proposed structures located in special flood hazard areas where base flood elevation data are utilized;

- Elevation in relation to mean sea level to which any  proposed structure will be flood proofed in accordance with Section 9.37 where base flood elevation data are utilized;

- Description of the extent to which any watercourse will be altered or relocated as a result of the proposed development and certification by a registered professional engineer that the flood carrying capacity of the watercourse will not be diminished; and

- A U.S. Army Corps of Engineer’s 404 Permit; as may be required.

- Landscape Plan – Major:  A Landscape Plan shall be submitted to the PEDD to coordinate review by City departments.  Proposed landscape treatment shall be indicated on the Major Landscape Plan and shall not be shown on any separately required Major Site Plan.  Landscape plans shall be submitted with Major Site Plans and Development Plans as required in Section 5.09.G.  Landscape plans may be submitted to the PEDD subsequent to Development Plan approval and prior to applying for CZC.  Each landscape plan shall be drawn to scale, show the placement of individual plants and include the following information in print as well as in digital format:

- Project name and address;

- Project owner’s name, address and telephone number;

- Name, address and telephone number of landscape architect;

- Distance from the property to nearest intersecting street;

- Signature panel for the PEDD;

- North arrow, scale (determined by the PEDD), date and/or date of revisions;

- A notation stating, “This landscape plan has been reviewed and approved by the owner/responsible agent who understands that any changes, substitutions, or deletions may require review and approval by the responsible reviewing authority” and a listing of proposed trees and plant material;

- The species (common name and botanical name), location and crown spread to scale of all trees existing on the site prior to construction with a caliper of six inches or greater at common breast height.  An indication of which trees are to be retained and which are to be removed, including a plan for how those to be retained will be preserved;

- Existing and proposed buildings and accessory structures to include existing and proposed signs;

- Zoning District boundaries and zoning designations of the site and adjacent properties;

- Parking and loading spaces showing all required wheel stops, curbs, including full-depth curbing around all internal parking lot landscaped islands, driveways, landscape screening, parking lot landscaping, and sidewalks or other pedestrian paths;

- All sight distance triangles;

- Location, width and names of all existing/proposed streets and watercourses;

- Right-of-way lines and property lines;

- All easements (provide dimensions and purpose);

- Location of all existing and proposed utilities, both overhead and underground;

- Location and type of trash disposal and details of screening;

- Location, height, type and material of all fences, walls, screen planting and landscaping details of all buildings and grounds.  Show each individual plant on the plan;

- Location of all ground mounted heating, ventilating and cooling equipment;

- Location of all transformers;

- Square footage measurements of the total site, building, parking and hard surface areas, and landscape areas.  Show percentage of landscape area for the total project.  For parking spaces, show percentage of interior landscape area;

- Dimensions and distances of landscape strips as required in Table 9.13;

- All landscaping materials shall meet the minimum specifications and standards as may be required by the PEDD and/or City Engineer;

- Grading plan, including mounding, and topographical lines at two one-foot intervals.

- Landscape Plan – Minor:  A Minor Landscape Plan shall be submitted to the PEDD to coordinate review by City departments.  Proposed landscape treatment shall be indicated on the Minor Landscape Plan and shall not be shown on any separately required minor site plan.  Landscape plans shall be submitted with minor site plans as required in Section 5.09.O.  Each landscape plan shall be drawn to scale, show the placement of individual plants and include the following information:

- Project name and address;

- Project owner’s name, address and telephone number;

- Name, address and telephone number of landscape architect;

- An indication of which trees are to be retained and which are to be removed, including a description of how those to be retained will be preserved;

- Existing and proposed buildings and accessory structures to include existing and proposed signs;

- Parking and loading spaces showing all required wheel stops, curbs including full-depth curbing around all internal parking lot landscaped islands, driveways, landscape screening, parking lot landscaping, and sidewalks or other pedestrian paths;

- All vehicle sight distance triangles;

- Location of all existing and proposed utilities, both overhead and underground, and easements;

- Location and name of all streets (public and private);

- Right-of-way lines and property lines;

- Grading, mounding and berming;

- Location and type of trash disposal and details of screening;

- Location, height, type and material of all fences, walls, screen planting and landscaping of all buildings and grounds;

- Location of all ground mounted heating, ventilating and cooling equipment and location of all transformers;

- Square footage measurements for the total site, building, parking and hard surface areas, and landscape areas; and

- Water features including drainage courses and any body of water, flood plain, and floodway route.

- Landscape Plan – Alternative:  Under certain conditions, the strict application of the regulations contained within this Section may be impractical.  In order to accommodate modifications to existing landscaping requirements, an Alternative Landscape Plan may be submitted to the PEDD.  An Alternative Landscape Plan may be submitted as part of an overall site plan in accordance with Section 5.09 N. for a Major Site Plan or Section 5.09 O. for a Minor Site Plan.  The Alternative Landscape Plan shall be provided at the time of submittal.  Said Alternative Landscape Plan and justification statement shall be forwarded to the PEDD for a recommendation, Requests for Alternative Landscape Plans will be accepted for review only when one or more of the following conditions apply:

- The site involves space limitations or is an unusually shaped lot;

- Topography, soil, vegetation, or other physical conditions of the lot are such that full compliance is impossible or impractical;

- Public safety considerations are involved; and

- Impact on the environmental quality of the lot and surrounding area will be improved with the proposed Alternative Landscape Plan.

- Lighting Plan:  A preliminary or a final Lighting Plan shall be provided at the time of submittal of any Development or Site Plan.  The plan shall be submitted along with other required site information to the PEDD to coordinate review by City departments.  A final Lighting Plan must be submitted to the PEDD subsequent to approval of any Development or Site Plan and prior to applying for CZC.

- Scaled building plans, site plans and elevations shall be submitted showing property boundaries, building location(s), parking lot layout, driveways, pedestrian pathways, all building entrances, adjacent right-of-way, north arrow, scale, address or legal description, and locations of all luminaries, controls, and electrical transformers.

- Cut sheets (profiles) shall be submitted for all proposed exterior luminaries and poles.

- Scaled iso-foot-candle plots and/or point-by-point foot-candle layouts shall be submitted demonstrating compliance.

- During the design and/or construction process after PEDD approval, changes shall be reviewed for re-approval prior to final acceptance.

- Preliminary Lighting Plans shall include exterior building, parking lot, and site lighting.  Sample cut sheets indicating pole and luminary height, color, temperature, as well as intensity of illumination in foot-candles on a point-by-point iso-foot-candle map shall also be provided

- Sign Plan:  A sign plan shall be provided at the time of the Development Plan or Site Plan submittal as may be required to assure compliance with the UDO, and will include:

- Name and address of the owner of the sign;

- Name and address of owner  or the person in possession of the premises where the sign is located or to be located;

- Clear and legible drawings showing the location of the sign(s) that are subject to the permit including the sign’s location with respect to existing right-of-way and property lines and all other existing signs that are on the same premises; and

- Drawings showing the dimensions, supporting structure, size, electrical wiring and components, sign materials, and method of attachment.

- Site Plan – Major:  An application form shall be completed by the developer/subdivider and submitted with the Major Site Plan.  The application form shall be provided by the PEDD.  The submittal requirements for a Major Site Plan include the following:

- Name and address of current property owner or designated agent;

- An accurate legal description prepared by, or certified by, a registered surveyor of the state;

- A property location map showing existing property lines, easements, utilities, and street right-of-ways;

- A site plan, prepared by a civil engineer, landscape architect or architect drawn at a suitable scale not to exceed one inch equals 100 feet indicating use, location, and height of existing and proposed buildings and structures, including accessory buildings, structures and uses, along with notation of the development standards for building spacing, setback from property lines, and maximum building heights along with a notation of the development standards for maximum building height.  The site plan should also show the location and conformation of off-street parking and loading areas, the arrangement of internal and in-out traffic movement including access roads and drives and the location of signs related to parking and traffic control;

- Topographic maps with sufficient elevations to show existing and generally proposed grading contours, major vegetation features, wooded areas and existing trees over six inches in diameter measured at the average breast height;

- Proposed landscaping plans indicating the preliminary description of the location and nature of existing and proposed vegetation, landscaping, screening elements and existing trees to be removed;

- Elevation drawings of proposed structures, floor plans, exterior construction materials, by type and color;

- Summary table showing total acres of the proposed development; number of acres devoted to each type of residential and/or non-residential use including street (right-of-way) and open space; number of dwellings;

- Building by type; total building square footage; and overall density (units per acre) and intensity (lot coverage);

- Preliminary grading and stormwater management plan;

- Preliminary landscape plan indicating location of existing plants; proposed plantings, including planting height and caliper of proposed trees measured at the average breast height;

- Other information necessary for the evaluation of existing site conditions and proposed development as deemed necessary by the PEDD and/or the Planning Commission; and

- Final Grading Plan, Lighting Plan, Landscape Plan, Sign Plan and overall Site Plan shall be provided at the time a Certificate of Zoning Compliance is sought.

- Site Plan – Minor:  The Minor Site Plan shall be provided at the time of submittal.  An application form shall be completed by the developer or subdivider and submitted with the Minor Site Plan.  The application form shall be provided by the PEDD.  Submittal requirements for a Minor Site Plan include the following:

- General layout plan with existing and proposed property lines, showing all proposed property lines with typical dimensions, yards and setbacks;

- Proposed and existing buildings on site with general sketch floor plans and building elevations;

- Building height shown on building elevation drawings including materials by type and color;

- List of property owners and labeling of adjacent property owners;

- Square footage of existing and proposed buildings;

- Zoning of property and existing use on site, including adjacent use and zoning;

- Final grading plan, stormwater plan and landscape plan;

- Street and parking lot layout, including street right-of-way, drive aisles, parking spaces, and sidewalk location; and

- Final water and sewer plan.

- Subdivision – Major:  An application form shall be completed by the developer/ subdivider and submitted with the Major Subdivision.  The application form shall be provided by the PEDD.  The following information shall be provided upon submittal of an application for a Major Subdivision:

- Major Subdivision – Preliminary Plat Application and Base Information:  An application form shall be completed by the developer/subdivider and submitted with the Preliminary Plat and required supplemental information.  The Preliminary Plat and base information shall be provided at the time of submittal.  The application form shall be provided by the PEDD.  The required fees shall also be paid at the time of application submittal.  The PEDD shall certify the receipt of a complete application package meeting the requirements of the UDO prior to scheduling the application on the Planning Commission agenda.  The Preliminary Plat shall be drawn on a 24-inch by 36-inch sheet(s) to a scale determined by the PEDD.  When more than one sheet is required, an index shall be incorporated into the title block.  The PEDD may approve the consolidation of the submittal requirements provided the intent of this Section is met.  The Preliminary Plat shall contain the following information at a minimum:

  - Name and address of developer, property owner or designated agent, land planner, landscape architect, engineer and/or surveyor;

  - Adjoining property owners, deed references and/or recorded subdivision names, recording references and adjoining property structures within 300 feet or as specified by the PEDD;

  - Vicinity map (section and range);

  - The ownership, acreage and boundaries of all adjacent properties within 300 feet of the subdivision or as specified by the PEDD.  If a recorded subdivision adjoins the subject site, the subdivision name, lot numbers and recording number shall be indicated with dashed lines;

  - North arrow;

  - Title block shall be in the lower right-hand corner.  The title block shall include title “Preliminary Plat”, sheet title, proposed subdivision name, developer and preparer, scale of the plan, tax map and parcel numbers, sheet index, date and revisions numbered and dated;

  - Boundary of the proposed subdivision clearly indicated by a heavy line with bearings and distances; and

  - Existing topography at two-foot intervals for slopes between two and 10 percent and at 10-foot intervals for slopes greater than 10 percent. Contour lines shall be indicated at least 50 feet beyond the subdivision boundary.  For slopes under two percent, one-foot contour intervals shall be shown.

- Preliminary Plat – Existing Conditions:  The Existing Conditions Map and text shall indicate the subdivision and all property within 200 feet of the subdivision or as specified by the PEDD, the following conditions depicted to scale:

- Existing generalized natural features, topographic map of existing site;

- Existing zoning;

- Existing utilities, including:  water, sanitary sewer and stormwater facilities, (indicating approximate pipe size and directions of slope); underground transmission lines; electric and telephone poles; street lights; fire hydrants; landfills; and public utility easements;

- Existing streets and roads, including:  locations, widths and names of all streets and roads; existing easements; and streets which have been preliminarily approved or recorded but which remain unimproved shall be indicated;

- Existing community facilities, including parks and recreation facilities.

- Preliminary Plat – Proposed Subdivision Plan:  The following proposed improvements are to be superimposed on tope of the Existing Conditions Map:

- Proposed generalized land use, including proposed building footprint(s);

- Proposed layout of all proposed and existing lots with approximate dimensions and minimum area in square feet (acres if lot size is greater than 100,000 square feet), section number, phase number and parcel number, building lines, lot frontages and required setbacks;

- Lot numbers in numerical order throughout the entire subdivision;

- The location, dimensions, use and area of all property proposed to be reserved or temporarily reserved for public use, or reserved for the use of all property owners in the subdivisions and the location, dimensions and purposes of any proposed easements; and

- Total number of lots, area of lots and parcels, area of public roadways, areas of public and private open space dedications, and total area of the subdivision.

- Preliminary Plat – Proposed Water, Sanitary Sewer, and Stormwater:  The following improvements are to be superimposed on top of the Existing Conditions Map:

- Proposed water system;

- Proposed sewer system;

- Proposed drainage and stormwater management systems, including:  the type of structures; drainage easements; proposed changes in topography; the 100-year floodplain (floodway and floodway fringe shall be indicated separately); and

- A preliminary storm drainage study including an evaluation of drainage structures and/or drainage systems, both upstream and downstream, affected by the drainage from the area covered by the Preliminary Plat, as directed by the City Engineer.

- Preliminary Plat – Proposed Circulation:  The following improvements are to be superimposed on top of the Existing Conditions Map:

- Proposed streets and roads, including:  widths of right-of-ways and pavements; tentative profiles of each street centerline; tentative horizontal curve data; and typical cross sections of each type of street proposed;

- Proposed sidewalks and bike paths, including:  locations; widths of right-of-ways; surface widths; and typical cross sections; and

- Proposed locations of street trees and landscape features.

- Preliminary Plat – Proposed Sedimentation and Erosion Control:  The following improvements are to be superimposed on top of the Existing Conditions Map:

- Locations and extent of tentative erosion and sedimentation control measures; and

- A Preliminary grading plan for the entire area covered by the Preliminary Plat.

- Final Plat:  The Final Plat shall include the subdivision design and layout in accordance with the approved Preliminary Plat or Development Plan.

- Final Plat – Construction Documents:  The Final Plat shall include a set of construction drawings and specifications of improvements.  This shall be a set of construction plans prepared by a registered professional engineer that shall include typical sections, plan and profile views, construction details, and estimates of quantities.  A set of construction drawings and specifications for all improvements shall be provided to the City Engineer.

- Final Plat – Security for Construction:  In lieu of constructing improvements, the subdivider may apply for Final Plat approval by insuring completion of the required improvements by one of the following methods and review and approval by the City Attorney, the City Engineer and the Finance Director.

- A surety performance bond and/or irrevocable letter of credit running to the City sufficient to cover the full cost of said improvements as estimated by the officials having jurisdiction, to assure the satisfactory installation of said improvements in accordance with its regulations;

- The subdivider may deposit with the City’s Director of Finance, the sum not less than the total estimated improvement cost, to be held in escrow to guarantee the satisfactory completion of said improvements within the required time, the form of said escrow agreement to be subject to the approval of the Director of Finance and the City Attorney and which agreement may provide for the making of payments from such funds from time to time upon certificates of the City Engineer that the balance remaining after such payments will, in his opinion, be adequate to pay the remaining costs of said improvements;

- The Subdivider may deposit with the Director of Finance a certified check in the amount of the total estimated improvement cost to be held in escrow until the satisfactory completion of construction, unless a default in the completion of said improvements occurs, in which event the check may be cashed by the Director of Finance and the proceeds thereof used to complete the improvements, to pay claims connected therewith for which the subdivider may be liable, or to cure any other default of the subdivider connected with the making of said improvements; and

- Inspection fee(s) shall be paid at the time of scheduling an on-site inspection.

- Final Plat – Construction of Buildings:  Construction of buildings shall not be permitted until all improvements are completed and accepted by the City.

- Final Plat – Regulations Concerning Improvements Required in Subdivisions:

- Required Minimum Improvements:  Minimum improvements shall be installed in the case of subdivisions within the City, in accordance with the requirements of the UDO.

- Time for Construction of Improvements:  All required improvements shall be constructed within two years of the acceptance of the Final Plat by the City Council.

- Street Construction:  Streets shall be graded to full width of the right-of-way and fully constructed with asphalt pavement or concrete pavements surfaced with asphaltic or Portland cement concrete wearing surfaces, concrete curbs and gutters with tile under-drain and porous backfill and proper storm drains and inlets.  Streets constructed within this City shall be in conformity with the plans and specifications for street construction adopted by Council, duplicates of which shall be kept on file in the office of the City Manager and the City Engineer.

- Water Supply:  Where a public water supply main is reasonably accessible, the subdivision shall be provided with a complete loop type water distribution system adequate to serve the area being platted, including a connection for each lot and appropriately spaced fire hydrants in accordance with the requirements of the Riverside Fire Department.  Water lines must be sized to provide sufficient fire flow to meet local fire department requirements.

- Storm Drainage:  Every subdivision shall be provided with a storm water sewer or drainage system adequate to serve the area being platted and otherwise meeting the requirements of Section 9.29.B Drainage of adjoining ground at a higher elevation must be included in stormwater design.

- Sewerage:  Where a public sanitary sewer main is reasonably accessible, the subdivision shall be provided with a complete sanitary sewer connected with such sewer main, including a lateral connection for each lot.

- Electric and Telephone Lines:  Where it is necessary to locate electric or telephone lines in the street right-of-way, said lines shall be buried, unless otherwise approved by the City Engineer, and shall be not closer less than nine feet six inches to the back of curb.

- Street Signs:  The City will erect the necessary street signs.  The subdivider shall reimburse the City for the cost thereof.

- Construction Plans:  Construction plans, including the following, for improvements shall be furnished in accordance with the specifications of the City Engineer and shall receive approval of the City Engineer and the Fire Department before improvements are installed, and before approval of the Final Plat:

  - The centerline or top of curb profile of each proposed street, with tentative grades indicated;

  - The cross-section of each proposed street, showing the width of pavement, the location and width of sidewalks and the location and size of the utility mains and thickness of materials specified;

  - The plans and profiles of proposed sanitary sewers and storm water sewers, with grades and sizes indicated, or method of sewage or storm water disposal in lieu of sewers;

  - A plan of the proposed water distribution system, showing pipe sizes and the location of valves and fire hydrants;

  - A drainage plan showing all existing and proposed storm sewers, manholes, catch basins, watercourses, culverts and other underground structures within the tract and immediately adjacent thereto, with pip sizes and grades, waterway openings indicated thereon.  The drainage plan shall show the method to be used for the adequate disposal of all storm water, including drainage outlets, and such other data as may be required by the City Engineer and Section 9.35; and

  - Submit worksheets showing that storm and sanitary pipe crossings and the design of catch basins at street low points.

- Inspection:  Prior to the start of any work covered by the above plans, after approval thereof and the payment of inspection fee(s), arrangements shall have been made to provide for inspection of the work sufficient, in the opinion of the City Engineer, to insure compliance with the plans and specifications as approved.

- Completion of Construction:  The construction of all improvements required by these rules and regulations must be completed within two years from the date of approval of the final plat by Planning Commission, unless good cause can be shown for the granting of an extension of time by authority of the Planning Commission.

- Maintenance After Approval:  For a period of one year from the date the constructed improvements were approved by the City Engineer the subdivider shall make such repairs or replacements as may be required and assured in the maintenance bond by reason of defective workmanship or material.

- Modification:  Where unusual or exceptional factors or conditions exist, the Planning Commission may modify any of the provisions of these regulations.

- Subdivision – Minor:  The Minor Subdivision shall be provided at the time of submittal.  An application form shall be completed by the developer/subdivider and submitted with the Minor Subdivision.  The application form shall be provided by the PEDD.  In order to be complete and to be accepted for review and processing, all Minor Subdivision (lot split) proposals must be legible and include or comply with the following:

- Name, address, telephone number, fax number and e-mail address of the existing property owner;

- Name, address, telephone number, fax number and e-mail address of the surveyor or preparer of the submittal if different from the property owner;

- Location and size of existing and proposed parcels, including date of creation of existing parcel to be split;

- North arrow and bar scale;

- Location information including:  location map; adjacent or frontage roads; adjacent parcel ownership; proposed easements of access; etc.;

- Acreage of all proposed lots and acreage of all remaining property resulting from the division of the original parcel, including existing and proposed boundaries;

- Proposed building envelope, building footprint and proposed site drainage and grading may be required by the TRC if existing data indicates a situation where development constraints should be addressed in detail sufficient for approving the development proposal;

- Site drainage and 100-year floodplain (floodway and floodway fringe, elevation and boundaries);

- Steep slopes, ravines, drainage swales, and all other natural features;

- All other natural and built features or conditions that in the determination of the PEDD is directly relevant to the ability of the proposed lot(s) to be buildable per these regulations.  Existing topography at two-foot intervals for slopes under 10 percent and 10-foot intervals for slopes greater than 10 percent or as approved by the TRC if topographic characteristics of the site and/or adjacent properties indicates a situation where development constraints should be addressed in detail sufficient for approving the development proposal;

- Any and all proposed easements, reserve areas or no-build zones; and

- A filing fee shall be charged and must be paid at the time that the final survey is filed with the PEDD.

- Temporary Use:  A Temporary Use application shall be provided at the time of submittal.  An application for a temporary use shall be filed with the PEDD on a form prescribed by the PEDD, along with the fee for such permit and the following information:

- A sketch plan showing the boundaries of the property;

- The use of adjacent properties identified and labeled;

- The location of the temporary use or structure on the property; and

- Location of all existing buildings, structures, parking lots, and other physical improvement on property.

5.15	Related Approvals:  Building and Occupancy Permit

- Building Permit

  - Definition:  A permit issued by the Chief Building Official authorizing the erection, construction, reconstruction, alteration, repair, conversion, or maintenance of any building, structure or portion thereof.  Such permit shall not be issued without the signature of the PEDD, certifying compliance with this UDO.

  - Process:  An application for a building permit shall be filed with the Chief Building Official on a form prescribed by the Chief Building Official, along with the fees and charges for building permits and inspections.  Each application for a building permit shall contain or be accompanied by such information and plans as required on the application form and as otherwise required by the Chief Building Official.  The PEDD and any other applicable departments shall review the application and any required plans in order to determine whether the proposed work complies with the applicable provisions of this UDO and all other applicable City ordinances and construction regulations.

- Certificate of Occupancy Permit:

- Definition:  A new building or part of a new building, an addition or enlargement of any existing building, or an existing building may be occupied after being altered or moved, and a change in use or occupancy of any building may be made in any existing building only after the Chief Building Official and PEDD has issued an occupancy permit stating that the building and/or the proposed use complies with the provisions of the UDO.  An occupancy permit shall be required for the purpose of maintaining, renewing, changing, or extending a use.

- Permit Process:  In issuing an occupancy permit the PEDD shall follow the requirements set forth in Section 5.11,B.

5.17	Variance Procedure

- Definition:  A variance may be granted allowing deviations from the height, mass, setback, parking, or other dimensional requirements established by the zoning and subdivision provisions of the UDO where practical difficulties unique to the property in question prevent full compliance with such provisions.

- Variance Process:  The BZA has the authority to grant variances.  The BZA may authorize, in specific cases, such variance from the terms of this UDO as will not be contrary to the public interest.

  - Pre-application Meeting:  The applicant may meet with the PEDD prior to submitting a variance request for consideration by to the BZA.  Following the conclusion of the meeting, the PEDD shall forward to the applicant a written summary of the results of the pre-application meeting including recommendations and all attached comments.

  - Preliminary Review by the PEDD:  Upon receipt of an application, the PEDD shall, within five days, review the application and determine whether it provides all necessary and required information.  If it is incomplete, the PEDD shall advise the applicant of the deficiencies and inform the applicant that no further action will be taken on the application until all necessary and required information has been provided.  If it is complete, the PEDD may forward the application to the TRC.

  - Variance Review by the TRC:  The TRC shall review the application after the PEDD determines that the application is complete and forward its comments within five days to the PEDD.  The PEDD shall forward copies of all documents filed with the PEDD to the BZA along with any report or recommendation of the TRC.

  - Variance Public Hearing and Notice by City Clerk of Council:  Within five days of determining that an application contains all the necessary and required information, the City Clerk of Council shall place the application on the agenda and schedule a public hearing on the proposed variance.  Notice of the hearing shall be provided at least once in one or more newspapers of general circulation in the City.  The notice shall be published at least five days before the date of the hearing.  The notice shall state the time and place of the hearing and a summary of the proposed Variance.  All documentation including any maps and plans shall be on file for public examination in the office of the PEDD.

  - Notice to Property Owners:  Written notice of the public hearing shall be provided to all owners of property within 300 feet of the subject parcel.  The applicant shall provide a list (available from the County Auditor’s current tax list) of the owners within 300 feet of the property for which the variance is requested to the PEDD.  Such notice shall be sent, by first class mail, at least 10 days before the date of the hearing addressed to the owners appearing on the County Auditor’s current tax list and to such other list or lists as verified by staff.

  - BZA Hearing:  The BZA shall conduct a public hearing and review the application.

  - BZA Action:  The BZA may approve the variance as requested; approve with modifications by the BZA; or deny the variance.  The BZA shall indicate the specific reason(s) for its recommendation.

  - Additional Conditions and Safeguards:  The BZA may further prescribe any conditions and safeguards that it deems necessary to ensure that the objectives of the regulations or provisions to which the variance applies will be met.

- Expiration of the Variance:  Variances shall expire one year from the date of enactment, unless prior thereto the applicant applies for a building permit in accordance with the granted variance.  There shall be no modification of variances except by further consideration of the BZA.  Extension of variances, without modification, may be applied for prior to the date of expiration, if the Variance does not carry a prohibition against the extension.  Extensions may be granted by the BZA if it finds that the requested extension is consistent with the purpose, policies, intent of, and the specifications of the UDO.  Requests for renewal of an expired Variance shall be considered to be the same as an application for a Variance and shall meet all requirements for application and review pursuant to Section 5.17.

- Standards for Approval:  The following factors shall be considered and weighed by the Planning Commission in determining practical difficulty or hardship:

- The granting of the Variance shall be in harmony with the general purpose and intent of the regulations imposed by this ordinance on the district in which it is located, and shall not be injurious to the area or otherwise detrimental to the public welfare;

- The granting of the Variance will not permit the establishment of any use which is not otherwise permitted in the district;

- There must exist unique circumstances or conditions applicable to the land or buildings where strict application of this ordinance would deprive the applicant reasonable use of his property.  Mere loss in monetary value shall not justify a Variance;

- There must be proof of hardship resulting from the strict application of this ordinance that was not created by the property owner.  Economic gain or profit is not sufficient proof that a Variance should be granted;

- The granting of the Variance is necessary for the reasonable use of land or buildings and the variance as granted is the minimum Variance that will accomplish this purpose;

- The granting of the Variance will not infringe on the rights of neighboring property owners to use their property, diminish property values, endanger the public safety, or create a public nuisance; and

- The granting of the Variance will not confer on the applicant any special privilege that is denied by this ordinance to other lands, structures, or buildings in the same zoning district.

- See Section 9.37 W. for additional standards as they apply to a variance from the Floodplain Design Standards.

- Submittal Requirements:  An application for a Variance shall be filed on a form provided by the PEDD, and shall be accompanied by the following requirements:

- Name, address, and phone number of applicant(s) and property owner or designated agent;

- Proof of ownership, legal interest or written authority;

- Legal Description of property or portion thereof;

- Description or nature of variance requested;

- Narrative statements establishing and substantiating the justification for the variance pursuant to Section 5.17, D;

- Site plans, floor plans, elevations and other drawings at a reasonable scale to convey the need for the variance;

- Payment of the application fee as established by City Council; and

- Any other documents deemed necessary by the PEDD.

5.19	Appeals Procedure

- Responsibility:  This Section identifies the responsibility for hearing appeals and establishes the appeals process for decisions made by the Administration and BZA.

  - Appeal of Administrative Action:  Any person adversely affected by any order, requirement, decision, or determination made by the PEDD, or a designated representative, in the administration or enforcement of the UDO may appeal to the BZA.

  - Appeals of Planning Commission Decisions:  Any person adversely affected by any order, requirement, decision, or determination made by the Planning Commission in the administration or enforcement of the UDO may appeal to the BZA.

  - Appeals of BZA:  Appeals of BZA decision shall be to the Montgomery Count Court of Common Pleas.

- Appeals to BZA:  The following outlines the appeals process and notification requirements for appeals to the BZA from an administrative decision:

- An appeal to the BZA may be taken by any person aggrieved or by a decision of the PEDD or the Planning Commission.  Such appeal shall be made within 10 days from the date of the action appealed from, by filing a notice of appeal with the City Clerk of Council.  The PEDD shall transmit to the BZA all the papers constituting the record upon which the action appealed from was taken.

- Upon the filing of the appeal, the City Clerk of Council shall give notice by one publication in a newspaper of general circulation at least 10 days before the date of the hearing and shall give notice of the hearing to the parties in interest.

- The BZA shall hear the application or appeal at its first meeting occurring after such required publication and notice.  It shall decide the case within 30 days from the date of such hearing and provide for its findings in writing.  At the hearing, any party may appear in person or be represented by an agent or attorney.